## Slide 1: DETERMINING INTRUDER AIRCRAFT POSITION USING SERIES OF STEREOSCOPIC 2-D IMAGES
Aditya Ramani
Thesis Supervisor: Dr. Atilla Dogan

## Slide 2: Outline
Introduction
Part 1: Camera Image Generation (incl. Simulation Results)
Part 2: Relative Position Calculation (incl. Simulation Results)
Conclusion and Future Work

## Slide 3: Introduction
Introduction of UAV (Unmanned Aerial Vehicles) into the NAS (National Air Space) requires the detect-and-avoid capability.
An aircraft should be able to detect other aircraft flying in the same airspace volume and make evasive maneuvers if there is potential conflict.
One potential method for intruder aircraft detection is processing digital images taken by onboard cameras
Avoidance algorithms could benefit from relative position information determined through image processing

## Slide 4: Introduction
Focus of thesis research is to compute the position of an intruder aircraft relative to an observer aircraft with onboard stereo cameras.
First phase of research effort was to generate camera images given the relative position information
This process uses a simple pinhole camera methods where cameras are characterized by focal length, angle of view and resolution.
The second phase of the research developed two methods to estimate the relative position based on the generated camera images. Both methods employ epipolar geometry of stereo vision based on two cameras placed on the aircraft with lateral separation.
Various cases were designed and run in MATLAB-Simulink environment to evaluate relative position estimation methods with different aircraft trajectories, different camera separation, and different image resolution

## Slide 5: Part 1: Camera Image Generation

## Slide 6: Reference Frames
Inertial Frame is defined to be located at geometrically-fixed point in space and its x, y, and z axes pointing local north, local east, and local down respectively (North-East-Down); referred to as I-frame
Body Frame of Aircraft-i defined to have origin at aircraft Center of Gravity, having axes definition as shown on diagram on the left; referred to as Bi-frame
Wind frame defined to have same origin point as Bi-frame and characterized by angle of attack α and side-slip angle β; referred to as Wi-frame

## Slide 7: Camera Frame
The camera-j frame is defined to have its origin at the center of the camera lens, and x-axis pointing along the normal line of view
Referred to as Cj-frame

## Slide 8: Rotation Matrices and Vectrix Formulation
Rotation matrices used to rotate from one frame to another.
RCjBi: rotation matrix used to rotate from the Cj-frame to the Bi-frame
RBiI: rotation matrix used to rotate from the I-frame to the Bi-frame
RBiWi: rotation matrix used to rotate from the Wi-frame to the Bi-frame
Vectrix notation used to write vector in terms of components in specified frame
Allows one to use the rotation matrix to transform vector representation to another frame

## Slide 9: Determining 3-D Position of Intruder Aircraft
First, the representation of velocity of each aircraft in inertial frame is written in terms of airspeed V , using the translational kinematics equation
The rotational kinematics equations are also used, expressed in terms of angles ψ, θ and Φ and pitch, roll, and yaw rates p, q, and r
These equations are implemented in Simulink

## Slide 10: Determining 3-D Position of Intruder Aircraft (cont.’d)
Using vector relations, the resulting equation that gives the representation of Aircraft 2 position relative to Aircraft 1 in B1-frame in terms of representations of Aircraft 1 and 2 in I-frame as:

## Slide 11: Transferring Relative Position to Images
Next step is to formulate Aircraft 2 relative to each camera at specified location and orientation relative to B1-frame
Using vector relations and rotation matrix from B1-frame to Cj-frame, the resulting equation is

## Slide 12: Transferring Relative Position to Images (cont.’d)
The next step is to formulate projection of intruder aircraft position in camera image plane
Ideal pinhole camera model used (see diagram on the right)
Camera aperture considered as a point, and no lenses used to focus light
Result is 2D matrix M (of size Nzj X Nyj, both of which are odd numbers) representing processed image file from digital camera
2 important camera parameters considered: focal length fcj and view angle γzj and γyj

## Slide 13: Transferring Relative Position to Images (cont.’d)
Position of point pB2 in Cj-plane is defined as

## Slide 14: Simulation Cases and Results
All cases below have several things in common:
A total of two cameras are used for each case.
The angle of attack and side-slip angles are [0 0]T for both Aircraft 1 and Aircraft 2 for each case.
γzj is 60 deg for each case.
The two cameras are aligned such that there’s no rotation relative to each other and the B1-frame
Unless otherwise noted, the camera position parameters are the same as those used in a NASA project dealing with a similar problem (”, ”,0”)
Unless otherwise noted, Ny=3839 and Nz=2159
Simulation time is 10 seconds for each case
For all cases, only the first 5 time instances where Aircraft 2 is visible on each camera is shown. Unless otherwise noted, time interval of points shown is 0.1 second

## Slide 15: Case 1
A simple case
Aircraft 1 and 2 are located at [0 0 0]T and [0 3 0]T respectively, and travel at speeds of 100 m/s and 105 m/s respectively
Both travel along a straight path, with Euler angles all set to 0 deg.
Starting Point

## Slide 16: Case 1 Image Results

## Slide 17: Case 2
This case has the same initial positions and speeds as case 1, but with yaw and pitch angles set to -1 and 1 deg respectively
Starting Point

## Slide 18: Case 2 Image Results

## Slide 19: Case 3
Both aircraft fly at same speeds as previous 2 cases (i.e., 100 m/s for Aircraft 1 and 105 m/s for Aircraft 2), but with Aircraft 2 flying both perpendicular to Aircraft 1 ant having its origin point at [600 -300 0]T
Starting Point

## Slide 20: Case 3 Image Results

## Slide 21: Case 4
This is a repeat of Case 1, but with increased later separation between the cameras. The cameras are now located 1.5 m to the right and left of B1-frame origin, with the other parameters remaining intact
In other words, (”, ,0”)

## Slide 22: Case 4 Image Results

## Slide 23: Case 5
This is a repeat of Case 2, but with modified image resolution
For this case, Ny=2001 and Nz=1001

## Slide 24: Case 5 Image Results

## Slide 25: Part 2: Relative Position Calculation

## Slide 26: Relative Position Calculation
Try to ‘reverse-engineer’ focuses on whether one could find the relative position of the intruder aircraft relative to the observer aircraft, assuming all that are given are the camera position(s) and orientation(s) relative to B1-frame and the images taken by at least two cameras at the same times
Show two methods to finding position, both of which use epipolar geometry of stereo vision, where two cameras view a single 3D scene from different positions

## Slide 27: Method 1: Triangular Angles
Use right-angled triangles and trigonometry to solve for intruder aircraft position relative to left camera (Camera 2) frame before using vector addition to solve for position relative to B1-frame
First solve for line of sight angle from camera-j to intruder aircraft using relationship between (iNy, iNz) and (γzj, γyj) using equations:

## Slide 28: Case A: ГBz2>0 and ГBz1>0
Aircraft located to the right of both cameras

## Slide 29: Case B: ГBz2>0 and ГBz1<0
Aircraft located somewhere in between the two cameras

## Slide 30: Case C: ГBz2<0 and ГBz1<0
Aircraft located to the left of both cameras

## Slide 31: Case D: ГBz2>0 and ГBz1=0
Aircraft located at center of camera 1 and to the right of camera 2

## Slide 32: Case E: ГBz2=0 and ГBz1<0
Aircraft located at center of camera 2 and to the left of camera 1

## Slide 33: Solving for zA

## Slide 34: Method 2: Virtual Image Frame Utilization
Given
Expressing in camera frame

## Slide 35: Method 2: Virtual Image Frame Utilization (cont.’d)
Since cameras are aligned with B1-frame, this means that:
Using similar triangles, one can deduce that:
This leads to: Finally, this gives

## Slide 36: Case 1

## Slide 37: Case 2

## Slide 38: Case 3

## Slide 39: Case 4

## Slide 40: Case 4 (Cont.’d)

## Slide 41: Case 5

## Slide 42: Case 5 (cont.’d)

## Slide 43: Conclusion
Both of the methods above give similar results, although the focal length method (Method 2) is more accurate as the plot 'follows' the real simulated values, while the values obtained on Method 1 veer away from the real simulated values with increasing distance.
As the distance between the 2 aircraft increase, the accuracy of the results obtained decrease. The accuracy is virtually non-existent if they are too far, as demonstrated in Case 3.
The accuracy of the result is also dependent on the baseline length (lateral separation). The larger the lateral separation, the more accurate the calculation.
The image resolution has negligible impact on the accuracy of the results obtained.
When distance increases, there are occurrences where the estimated position stay constant while the actual position increases.
As the aircraft travels farther and farther away, the disparity between image points decrease; this is the root cause for drop in accuracy with increasing distance.

## Slide 44: Future Work
In all, it can be seen that it is indeed possible to obtain useful position estimation results given that the intruder aircraft was visible on both cameras at once and was reasonably close to observer aircraft
Future methods that could improve results include
Use actual images rather then creating binary ones
Use stereo camera setup with cameras at various orientations and positions
Increase complexity of simulation cases